## Slide 1: Advancing Cloud Computing Capabilities on gem5 by Implementing the RISC-V Hypervisor Extension
University of Athens, Greece
Nikos Karystinos
D Dimitris Gizopoulos
George-Marios Fragkoulis d
George Papadimitriou
CARRV 2024
Sunday, 3 November

## Slide 2: Background: the gem5 simulator
gem5 is a state-of-the-art microarchitectural simulator
  Utilized in academia and industry (AMD, Arm)
  Simulates many ISAs like Arm, x86 and RISC-V
  Simulations without OS (Syscall Emulation) and with OS (Full System)
  Many configurable hardware components like
    CPU models (In Order, Out of Order)
    Caches (capacity, associativity, topologies)
    Peripherals (UART, Network Adapter)
    DRAM

## Slide 3: Background: RISC-V in gem5
[CARRV 2017] RV64G ISA implemented (base instruction set) Alec Roelke, Mircea R. Stan (University of Virginia)
[CARRV 2021] RISC-V FS simulation support Peter Yuen Ho Hin, Liao Xiongfei, et. al. (Huawei)
Extensions relevant to cloud-computing
[2022] Bit Manipulation (Zb) Jerin Joy
[2023] Cryptography (Zk) Roger Chang
[2023] Vector (Zv) Adrià Armejach, Xuan Hu, Jerin Joy, Roger Chang, Hoa Nguyen and others
The missing piece: H (hypervisor) extension Cannot run guest VMs efficiently without this!!!

## Slide 4: Background: RISC-V Hypervisor (H) Extension
H extension supports the efficient hosting of a guest OS
  Virtualizes the supervisor-level architecture
Registers
  26 new CSRs
Interrupts & Exceptions
  9 new exception codes (4 new interrupts + 5 new exceptions)
Two-stage Translation
  G-stage Walking for guest physical to host physical translation
Hypervisor Instructions
  20 new instructions including memory fences and special memory instructions for hypervisor

## Slide 5: Background: RISC-V Hypervisor (H) Extension
Firmware
OS
User Space
M
S
1
0
3
U
Firmware
Host User Space
M
1
0
3
U
2
Hypervisor
Without H-extension
With H-extension
HS
Guest User Space
VU
Guest OS
VS
Virtualized Environment
Non-Virtualized Environment

## Slide 6: Contributions
We implement the H extension into the latest gem5 (v24.0)
  Pull request is currently under review
We assess the functional correctness of our implementation
  H extension tests behave equivalently on Spike (reference ISA simulator)
  Ran Xvisor (a type-1 hypervisor) and guest VMs
We provide insights into the H extension’s impact on performance

## Slide 7: Implementation
Registers
  26 new CSRs
Interrupts & Exceptions
  9 new exception codes (4 new interrupts + 5 new exceptions)
Two-stage Translation
  G-stage Walking for guest physical to host physical translation
Hypervisor Instructions
  20 new instructions including memory fences and special memory instructions for hypervisor

## Slide 8: Implementation Methodology: Registers
16 bits (HIP CSR)
mtip
0
stip
0
msip
0
ssip
0
seip
0
meip
0
000
…
64 bits (gem5 physical register)
0
1
2
3
4
5
6
7
8
9
10
11
13
15
63
0
12
vssip
vstip
vseip
sgeip
16 bits (MIP CSR)
0
0
0
0
0
0
Additional H extension bits
Original bits
Control Status Register (CSR)
Physical Register
Problem: HIP should see purple bits only
Solution: Read/Write masks nullify the rest
of the bits!

## Slide 9: Implementation Methodology: Registers
Linux (native – S mode)
Linux (guest – VS mode)
Read sstatus
Read sstatus
csrr t2, sstatus
csrr t2, sstatus
OK!
t2 = sstatus;
OK!

t2 = vsstatus;

## Slide 10: Implementation
Registers
  26 new CSRs
Interrupts & Exceptions
  9 new exception codes (4 new interrupts + 5 new exceptions)
Two-stage Translation
  G-stage Walking for guest physical to host physical translation
Hypervisor Instructions
  20 new instructions including memory fences and special memory instructions for hypervisor

## Slide 11: Implementation Methodology: Exceptions
Created new fault types
  Virtual Supervisor and Guest interrupts
  Guest-Page Faults
  Virtual Ecall
Extended gem5’s fault handling functionality
  Handled faults in the correct privilege levels based on values of new delegation registers (e.g. hideleg, hedeleg)

## Slide 12: Implementation
Registers
  26 new CSRs
Interrupts & Exceptions
  9 new exception codes (4 new interrupts + 5 new exceptions)
Two-stage Translation
  G-stage Walking for guest physical to host physical translation
Hypervisor Instructions
  20 new instructions including memory fences and special memory instructions for hypervisor

## Slide 13: Background: RISC-V Address Translation
Supports classic paged virtual memory
  different address width translation schemes: Sv32, Sv39, Sv48
  gem5 implements Sv39 (39-bit virtual addresses) for now
H extension adds another translation stage (G-stage)

## Slide 14: Background: Sv39 Scheme
VPN2
VPN1
VPN0
offset
L0 PTE
L0 Page Table
L1 PTE
L2 PTE
data
PFN (44 bits)
0
11
12
20
21
29
30
38
9 bits
4KB Page
L1 Page Table
L2 Page Table
satp
9 bits
9 bits
PA
Virtual Address
Physical Address
(Lives in RAM)

## Slide 15: Background: Two-Stage translation
Guest Virtual Address
gPPN2
gPPN1
gPPN0
L0 PTE
L1 PTE
L2 PTE
PFN (44 bits)
hgatp
40
0
11
12
20
21
29
30
G-stage (2nd stage)
Host Virtual Address
VS-stage (1st stage)
gVPN2
gVPN1
gVPN0
offset
L0 gPTE
L0 Page Table
L1 gPTE
L2 gPTE
gPFN (44 bits)
0
11
12
20
21
29
30
38
39-bit Guest Virtual Address
9 bits
4KB Page
L1 Page Table
L2 Page Table
vsatp
9 bits
9 bits
data
Host Physical Address (Lives in RAM)
Guest Physical Address (Host Virtual Address)
Guest Virtual Address

## Slide 16: Implementation Methodology: Translation
Extended page walking logic to support new types of walks
  G-stage
  Two-stage
    Virtual First Stage (guest virtual → guest physical)
    G-stage as Second Stage (guest physical → host physical)
Extended permission checking based on effective prv and V
  G-stage accesses are always checked as if prv == PRV_U
  Special Hypervisor memory instructions are executed as if V == true
  New page-fault types (e.g. guest load page fault)

## Slide 17: Implementation
Registers
  26 new CSRs
Interrupts & Exceptions
  9 new exception codes (4 new interrupts + 5 new exceptions)
Two-stage Translation
  G-stage Walking for guest physical to host physical translation
Hypervisor Instructions
  20 new instructions including memory fences and special memory instructions for hypervisor

## Slide 18: Implementation Methodology: Instructions
Extended ISA specification files with the new instruction implementations
  new fences (HFENCE, HINVAL) → selectively flushes TLB entries
  new loads & stores (HLV, HLVX, HSV) → hypervisor accesses memory as if the request originates from a virtualized guest
New memory instruction formats for hypervisor loads & stores

## Slide 19: Implementation Methodology: Validation
Public Tests for H extension
Exceptions & HLV/HSV
Two-Stage Translation
Registers

## Slide 20: Implementation Methodology: Validation
Run a hypervisor and a guest VM
  If the guest VM’s OS boots up and can execute programs
    we gain strong confidence in the correctness of our implementation
We choose to run Xvisor (a type-1 or baremetal hypervisor)
Xvisor Mascot

## Slide 21: Implementation Methodology: Validation
Xvisor boot video
Notes: Xvisor boot video

## Slide 22: Experimental Results
We obtain results from nine benchmarks from MiBench Suite
The programs’ full-system execution is simulated in gem5
  Natively (no virtualization)
  In a VM (virtualized environment)
We examine the following three types of simulation overheads
  Simulation Time overhead
  Instruction overhead
  Exception Handling overhead

## Slide 23: Experimental Results: Time Overhead
~50% slowdown on average

## Slide 24: Experimental Results: Instructions Overhead
~5% more instructions on average

## Slide 25: Experimental Results: Exceptions Overhead
Exceptions handled in S in native execution and in VS during guest execution
are equivalent

## Slide 26: Conclusion & Future Work
H extension implementation in gem5 is functional and stable
  It will be merged in some next version of gem5
Future Work
  Support all simulated CPU types of gem5
  Run various other hypervisors (e.g. type-2 hypervisor like KVM)
    This further validates our implementation
    Evaluate performance tradeoffs
  Perform comprehensive microarchitectural design space exploration for cloud deployments

## Slide 27: Thank you! Questions?
University of Athens, Greece
George-Marios Fragkoulis d
George Papadimitriou
Nikos Karystinos
D Dimitris Gizopoulos
CARRV 2024
Sunday, 3 November