## Slide 1: GPGPU Pipeline Visualization for RISC-V SIMT Architecture
CARRV 2024
Yu-Yu Hsiao†, Liang-Chou Chen, Chung-Ho Chen
National Cheng Kung University, Taiwan
†n28111534@gs.ncku.edu.tw

## Slide 2: Outline
Motivation
  RISC-V-based GPGPUs
  Pipeline Visualization for CPUs
Pipeline Visualization for RISC-V SIMT Architecture
  Enabling SIMT Execution Model on RISC-V
  Case Studies

## Slide 3: RISC-V-based GPGPUs
Simty (CARRV 2017)
  Dynamic inter-thread vectorization
  FPGA prototype
  Written in synthesizable VHDL
Vortex (CARRV 2019, MICRO 2021)
  LLVM-based software stack for OpenCL
  Texture and graphic support
  FPGA prototype
  Written in synthesizable SystemVerilog
  Incorporates a cycle-level simulator (C++)
GPGPU architecture exploration for CUDA:
GPGPU-Sim (ISPASS 2009)
Accel-Sim (ISCA 2020)

## Slide 4: Pipeline Visualization for CPUs (1/2)
Pipeline visualization has become a well-established technique in the CPU architecture domain
  gem5 text-based pipeline view, AndesClarity, Konata

## Slide 5: Pipeline Visualization for CPUs (2/2)
Example: Dhrystone running on a RISC-V out-of-order superscalar processor, RSD1
  Superscalar pipeline: Two instructions are executed simultaneously at the same stage
  Out-of-order execution: Instructions are executed out of program order
  In-order fetch and retirement: Despite being executed out-of-order, the instructions are fetched and committed in the program order
1https://github.com/rsd-devel/rsd

## Slide 6: SPMD on SIMT Machine
Load
Load
Add
Store
iter. 0
iter. 1
time
…
Load
Load
Add
Store
Warp 0 at PC X
Assume:
thread/warp = 32
iteration/thread = 1
Scalar inst.
Warp: A set of threads that executes the same instruction (i.e., at the same PC)
// tid [0,N)
C[tid] = A[tid] + B[tid];

## Slide 7: SPMD on SIMT Machine
Load
Load
Add
Store
iter. 32
iter. 33
time
…
Load
Load
Add
Store
Warp 1 at PC X
Assume:
thread/warp = 32
iteration/thread = 1
Scalar inst.
Warp: A set of threads that executes the same instruction (i.e., at the same PC)
// tid [0,N)
C[tid] = A[tid] + B[tid];
All warps in a SIMT machine are scheduled and executed seamlessly in a fine-grained multithreaded pipeline

## Slide 8: The Branch Divergence Issue
Each thread can have conditional control flow instructions
Threads in the same warp can execute different control flow paths
BB_0
// BB_0
if (tid % 2 == 0) {
// BB_1
} else {
// BB_2
}
// BB_3
BB_1
BB_2
BB_3
Priority
Active Threads
SIMD
Utilization

## Slide 9: ICS-First Re-convergence Scheme1
Idea: Give inner conditional statements a higher priority
  Faster threads will pause and wait for reconvergence at the outer statement due to priority degradation
BB_0
// BB_0
pri_raise();
if (tid % 2 == 0) {
// BB_1
} else {
// BB_2
}
pri_lower();
// BB_3
BB_1
BB_2
BB_3
Priority
P0
P1
P0
Active Threads
SIMD
Utilization
100 %
50 %
50 %
100 %
pause
re-converge
1Kuan-Chung Chen and Chung-Ho Chen. 2018. Enabling SIMT Execution Model on Homogeneous Multi-Core System. ACM Transactions on Architecture and Code Optimization, 15, 1, (Mar. 22, 2018), 6:1–6:26. doi: 10.1145/3177960.

## Slide 10: Proposed ISA Extension for our GPGPU
We employ ICS-First algorithm to handle branch divergence
3 additional instructions using custom-1 opcode
Patched LLVM compiler for inserting priority adjustment instructions automatically
fsa.pri.raise
fsa.pri.lower
fsa.pri.reset

## Slide 11: RISC-V SIMT Pipeline Architecture
Microarchitecture of modeled SM
  Based on the architecture of GPGPU-Sim and CASLab-GPU1
  8-stage in-order issue OoO commit pipeline, priority-based PC arbitration
  Dedicated fetch scheduler
1Y. -X. Su, J. -H. Jheng, D. -J. Chen and C. -H. Chen, "Development of an Open ISA GPGPU for Edge Device Machine Learning Applications," 2019 Eleventh International Conference on Ubiquitous and Future Networks (ICUFN), Zagreb, Croatia, 2019, pp. 214-217, doi: 10.1109/ICUFN.2019.8806196.

## Slide 12: Pipeline Visualization Workflow
We implement a cycle-based RISC-V SIMT simulator
Run execution-driven simulation on a compiled SPMD program
Logs are dumped during the simulation
Open and render the pipeline trace in Konata pipeline viewer
Kanata 0004
C= -1
C 1
I 0 0 0
S 0 0 F1
I 1 0 0
S 1 0 F1
C 1
I 2 0 0
S 2 0 F1
I 3 0 0
S 3 0 F1
C 1
C 1
...
Kanata Log Format
Log size:
w/o compression: 200 bytes per instruction
w/ compression (gz): 40 bytes per instruction

## Slide 13: Pipeline Visualization for SIMT Architecture (1/2)
In SIMT, instructions in the pipeline may belong to different warps
  Use different colors to identify the warp ID of the instruction
To trace the execution of individual instructions throughout the pipeline
  Use different colors to identify the pipeline stage (just as CPUs)

## Slide 14: Pipeline Visualization for SIMT Architecture (2/2)
Meaning of the generated pipeline trace color scheme and symbol

## Slide 15: Case Study (1/3): Handling Control Divergence
We reproduce the situation mentioned earlier with the assembly code
  Branch taken: BB_1
  Not taken: BB_2
.section .text
.global main
main:
bb0:
csrr a0, 0xfe2 # read tid
andi a0, a0, 1 # tid % 2
fsa.pri.raise
beqz a0, bb1
bb2:
slli a0, a0, 1
j bb3
bb1:
addi a0, a0, -1
bb3:
fsa.pri.lower
ret

## Slide 16: Case Study (1/3): Handling Control Divergence
Flushed instructions
control dependency

## Slide 17: Case Study (1/3): Handling Control Divergence
BB_0
control dependency

## Slide 18: Case Study (1/3): Handling Control Divergence
BB_1 -> BB_3
control dependency
diverged!
Threads in the same warp diverged
SIMD utilization rate: 50%
When reaching fsa.pri.lower, the execution pauses and resumes at the other divergent path

## Slide 19: Case Study (1/3): Handling Control Divergence
BB_2
control dependency
SM continues to execute the other divergent path
Threads in the same warp still diverged (with mask inverted)

## Slide 20: Case Study (1/3): Handling Control Divergence
BB_3
control dependency
re-converge
All threads now share the same priority (P0), resulting in re-convergence

## Slide 21: Case Study (1/3): Handling Control Divergence
ICS-First algorithm handles branch divergence effectively
Control dependencies have a great impact on performance
  SIMT processor should be able to hide the latency of control flow changes by proactively scheduling distinct warps for execution
control dependency

## Slide 22: Case Study (2/3): Latency Hiding Through TLP
Stream Multiprocessors (SM) utilize concurrency to hide latencies
  If one warp stalls, the SM can efficiently use fine-grained multi-threading to switch to another warp
  Higher Thread-Level Parallelism (TLP)
ref: https://dl.acm.org/doi/10.1145/2807591.2807598
GTO: Greedy-Than-Oldest

## Slide 23: Case Study (2/3): Latency Hiding Through TLP
Demo: A load-use-store code snippets
data dependency
data dependency
data dependency
Configuration:
8 warps per core
4 threads per warp
GTO scheduler
Latency hiding by scheduling other warps for execution (high TLP)

## Slide 24: Case Study (2/3): Latency Hiding Through TLP
Demo: A load-use-store code snippets
Configuration:
2 warps per core
16 threads per warp
GTO scheduler
data dependency
Latency is exposed and stalls the pipeline (low TLP)

## Slide 25: Case Study (2/3): Latency Hiding Through TLP
Demo: A load-use-store code snippets
The slope of the trace roughly indicates the IPC performance
  Steeper: Instructions are issued and committed more frequently (higher IPC)
  Flatter: Pipeline is stalled due to the presence of long-latency instructions (lower IPC)

## Slide 26: Case Study (3/3): LRR & GTO Scheduling Policies
Loosely Round Robin (LRR)
  Warps are prioritized for scheduling in round-robin order
  “Loosely”: If a warp cannot issue during its turn, the next warp in round-robin order is given the chance to issue
Greedy-Then-Oldest (GTO)
  Prioritizes the execution of a single warp until it encounters a blocking latency event

## Slide 27: Case Study (3/3): LRR & GTO Scheduling Policies
We run the same workload with LRR and GTO
  GTO: The load-use-store program hotspot is scattered
  LRR: All warps reach the hotspot concurrently
Hotspot of warp 0
warp 1
warp 2 & 3
Hotspots occur concurrently
Configuration:
4 warps per core
8 threads per warp
GTO scheduler

## Slide 28: Case Study (3/3): LRR & GTO Scheduling Policies
The concurrent occurrence of program hotspots can potentially stall the pipeline (workload: 2mm)
The execute stage becomes congested
Long-latency instructions are temporally separated
Instructions cannot be issued due to the stall

## Slide 29: Conclusion and Future Work
Pipeline visualization is also helpful for SIMT architectures
  Architecture exploration
  Performance bottleneck analysis
  Education in computer architecture
Rendered pipeline trace can serve as a reference model for RTL implementations
  Validate the behavior of the implementation
  Improve the accuracy of the cycle-based model
Integration to SOTA GPU simulation platforms (Accel-Sim)

## Slide 30: Thank you!